## Slide 1: Identify Types of Devices Connected to 802.11 WiFi
Swapnil Samant
CS 5390 – Wireless Networks
Spring 2018
UTEP
04/30/2018

## Slide 2: Information Available
MAC Address
DHCP Fingerprint
MAC Sublayer Management Entity (MLME)

## Slide 3: MAC Address
IEEE OUI (http://standards-oui.ieee.org/oui.txt)

## Slide 4: DHCP Fingerprint
Parameter request list (Discover and Request Packets from client)
Option 55:
  1 – Subnet Mask
  6 – Domain Name Server
  15 – Domain Name
  3 – Router
  33 – Static Route
  e.g. 1,6,15,44,3,33,150

## Slide 5: DHCP Fingerprint - Fingerbank

## Slide 6: MAC Sublayer Management Entity (MLME)
Types of MLME frames
  QoS Data Frames,
  Acknowledgement frames,
  Request-to-send frames,
  Clear-to-send frames
  Probe Request
  Probe Response
  Association frames
Set of Fixed Parameters
Tagged parameters (Required and optional)
  optional fields implemented as Type-­Length-­Value tuples

## Slide 7
https://media.defcon.org/DEF%20CON%2025/DEF%20CON%2025%20presentations/DEFCON-25-Denton-Gentry-I-Know-What-You-Are-By-The-Smell-Of-Your-Wifi-UPDATED.pdf

## Slide 8
https://media.defcon.org/DEF%20CON%2025/DEF%20CON%2025%20presentations/DEFCON-25-Denton-Gentry-I-Know-What-You-Are-By-The-Smell-Of-Your-Wifi-UPDATED.pdf

## Slide 9: MLME – Probe Request Frame
iPhone SE
wifi4|probe:0,1,50,3,45,127,107,221(0017f2,10),221(0050f2,8),221(001018,2),htcap:4021,htagg:17,htmcs:000000ff,extcap:0400088400000040|assoc:0,1,50,33,36,127,221(0017f2,10),221(001018,2),txpow:1402,extcap:0000000000000040

## Slide 10: Setup

## Slide 11: Applications
Link quality management for access points
Intrusion detection
Enterprise BYOD management

## Slide 12: References
Passive Taxonomy of Wifi Clients using MLME Frame Contents. Google, Inc., 2016.
DEF CON 25 Conference - Denton Gentry - I Know What You Are By the Smell of Your Wi-Fi https://www.youtube.com/watch?v=n_gSJkswdhU
https://github.com/NetworkDeviceTaxonomy/wifi_taxonomy

## Slide 13: Thank you!
Questions??